## Slide 1
AUTOMATED PAINTING ROVER
Autonomous AI Navigation &
Intelligent Painting-Control Software
Software Subsystem — Design Review
Anurag University | Ref: INC25ETS084848 | Concept Phase — WBS 1.1 / 1.2
Notes: Open by framing scope precisely: this deck covers the SOFTWARE subsystem of APR only — Autonomous AI Navigation and painting control — not the mechanical or electrical design. Emphasize this is a design review, not a finished product demo: the goal is to show the team understands what it is building, why, and how it will be tested. Technical point to land: the whole deck follows one rule — AI never touches motors, spray, or vacuum directly; classical robotics does the safety-critical work. Likely question: 'Is this software already implemented?' Strong answer: 'No — this is the design and architecture that Phases 0-14 of our roadmap will implement, simulation-first, with clear completion criteria for every phase.'

## Slide 2
MOTIVATION
Problem & Software Objectives
APR — Autonomous AI Navigation & Painting Control | Design Review
2
THE PROBLEM
Manual painting of large / vertical / hazardous structures is slow, inconsistent, and risky for workers at height or near toxic fumes.
Worker safety exposure at height & to fumes
Inconsistent coat thickness and coverage
No data trail for QA / compliance
Slow throughput on large façades
SOFTWARE OBJECTIVES
Convert a CAD wall drawing into an executable coverage plan
Navigate autonomously with ±20 mm path accuracy
Hold 200–300 mm standoff and gate spray in real time
Detect obstacles and replan without human input
Enforce a safety supervisor that outranks every other module
Stream live telemetry and produce an auditable KPI log
Notes: Left side: ground the audience in why this project exists — worker safety and quality consistency, drawn straight from WBS 1.1's use-case rationale. Right side: these six objectives are the spine of the entire rest of the deck — each later slide maps to one or more of them. Technical point: every objective here is measurable (±20mm, 200-300mm, etc.) — not vague aspiration, per WBS 1.2's explicit instruction to avoid statements like 'fast enough'. Likely question: 'Which objective is hardest to hit?' Strong answer: 'Path accuracy at ±20mm while fused localization is still maturing — that's why Phase 4 has its own dedicated drift-budget test before we touch coverage planning.'

## Slide 3
TRACEABILITY
Design Requirements
APR — Autonomous AI Navigation & Painting Control | Design Review
3
Requirement | Target | Source
Path accuracy | ±20 mm / 1 m | Dev. Plan
Coverage rate | ≥ 10 m²/hr, ≥90% uniform | WBS 1.2 §3
Standoff | 200–300 mm, ±20 mm | Dev. Plan
Paint thickness | 50 µm ± 15 µm | ARP-Req. §3
E-stop reaction | ≤ 0.5 s | WBS 1.2 §5
Battery runtime | ≥ 4 hr continuous | WBS 1.2 §4
Overspray waste | ≤ 10% | WBS 1.2 §3
Requirement
Target
Source
18 REQUIREMENTS TOTAL
Every number on this slide is traced directly to WBS 1.1 Success Criteria or WBS 1.2 Requirements Definition — none is invented for this presentation.
Open items still TBD:
• Fall-detection threshold (kPa/N)
• Vacuum pump vs. 15 kg payload
• Steering: skid-steer vs. articulated
Notes: Walk the table top to bottom quickly — don't read every cell, just anchor that these are measurable, testable numbers, not adjectives. Technical point: full traceability matrix (18 requirements) is in the written report Part 2; this slide is the condensed version for the review. Likely question: 'Where did the 50µm ±15µm thickness number come from — the WBS doc said ±0.5mm.' Strong answer: 'The updated ARP-Requirements document tightened that to 50µm±15µm dry film — we're carrying the updated figure, and both are traced in the written report.' Be ready to admit the three open TBD items plainly if asked — that's expected at this stage, not a weakness.

## Slide 4
SYSTEM DESIGN
Overall Software Architecture
APR — Autonomous AI Navigation & Painting Control | Design Review
4
CAD /
DXF
Digital
Wall Map
Mission
Planner
Coverage
Planner
Localization
(EKF)
Nav2
Navigation
Obstacle
Detection
Motion
Controller
Standoff
Controller
Spray
Controller
Telemetry /
Dashboard
SAFETY SUPERVISOR
Sits above every module in this diagram — not just another node in the chain. Can force a hard stop on Navigation, Motion, and Spray regardless of what they are requesting.
Inputs it monitors: E-stop • vacuum pressure • tilt • slip • battery • comms • sensor health • navigation health
Key principle: Coverage Path Planning ≠ Navigation. Coverage decides what to paint and in what order; Navigation decides how to safely move along that plan. AutoCAD never drives the rover directly — it only produces geometry.
Notes: Talk through the three rows left to right, top to bottom — this is the full pipeline from CAD file to spray gun, in the order data actually flows. Spend the most time on the Safety Supervisor box: it's drawn separately on purpose because it is NOT part of the sequential pipeline — it's an arbiter that can interrupt any box at any time. Technical point: emphasize the boxed callout at the bottom — reviewers often conflate coverage planning and navigation, so pre-empt that question here. Likely question: 'Why not let Nav2 handle coverage planning too, since it does path planning already?' Strong answer: 'Nav2's planner is built for point-to-point navigation, not full-area coverage optimization — Boustrophedon coverage generation is a different problem class, so we keep it as its own action server and only hand Nav2 the resulting waypoints.'

## Slide 5
GEOMETRY PIPELINE
CAD/DXF → Digital Wall Map
APR — Autonomous AI Navigation & Painting Control | Design Review
5
DWG/DXF
file
CAD
Parser
Geometry
Extraction
Wall +
Openings
Coordinate
Transform
Digital
Wall Map
WHAT'S EXTRACTED
Outer wall boundary polygon (mm→m)
No-paint regions: windows, doors, fixtures
Wall height / width / reference origin
Optional surface-type tag per CAD layer
IF CAD & SENSORS DISAGREE
Live sensor observation always wins for obstacle avoidance
Discrepancy flagged as unverified_region in the map
Affected sub-area is queued for operator confirmation
Notes: Walk the six-box pipeline once, left to right — this is a deliberately boring, linear, auditable process, which is the point: nothing here is a black box. Left card: name the concrete outputs of parsing — a boundary polygon plus tagged no-paint polygons, all converted from CAD units into meters in a wall-local frame. Right card: this is the most reviewer-tested part of this slide — show that the design has already thought about CAD being wrong or stale, not just the happy path. Technical point: CAD is pre-mission, offline, and produces a static map — it is never read live while the rover paints. Likely question: 'What if there is no CAD file at all for a wall?' Strong answer: 'Out of scope for this prototype by design — the use-case assumes a CAD-mapped wall; a sensor-only fallback is listed explicitly as future work, not quietly assumed to work.'

## Slide 6
PLANNING LAYER
Mission Planning + Coverage Path Planning
APR — Autonomous AI Navigation & Painting Control | Design Review
6
MISSION PLANNER
Splits a job into ordered wall segments
Requests a coverage path per segment
Tracks state: pending → in_progress → painted
Owns mission state machine, subordinate to Safety Supervisor
effective_spacing = spray_width × (1 − overlap)
Example: 0.30 m width, 50% overlap → 0.15 m between passes
Boustrophedon (zig-zag) is the baseline pattern — alternating passes, transition waypoints between rows, no-paint regions clipped out.
ZIG-ZAG COVERAGE (top view)
no-paint
region
Waypoints tagged spray_active = true/false; transitions between rows are non-spray moves.
Notes: Left card: Mission Planner is deliberately 'thin' — it sequences and tracks, it does not compute geometry itself; that separation is the point of this slide's title pairing the two together. Point at the formula box and work the example out loud: 0.30m spray width, 50% overlap, gives 0.15m row spacing — this is exactly the calculation the Coverage Planner runs at planning time. Right side: the zig-zag diagram is the actual pattern the planner generates; the orange block shows a no-paint region and how a row gets clipped/split around it. Technical point: coverage validity (≥90%) is checked at planning time by summing pass footprint area against the paintable polygon — not verified after the fact. Likely question: 'Why alternate direction each row instead of always returning to the same side?' Strong answer: 'It minimizes non-productive transition travel — a return-to-start pattern would roughly double transit time between rows.'

## Slide 7
STATE ESTIMATION
Localization + Sensor Fusion
APR — Autonomous AI Navigation & Painting Control | Design Review
7
Encoders
High-rate relative odometry
Weakness: Slips on wet/painted surface
IMU
Orientation, angular rate, tilt
Weakness: Drifts without correction
LiDAR
Absolute scan-match correction
Weakness: Weak on featureless flat walls
Camera
Visual context (optional)
Weakness: Lighting-dependent
EKF FUSION (robot_localization)
Encoders
+ IMU
(~50 Hz)
LiDAR scan-
match (~5-10 Hz)
correction
/odometry/filtered — bounded-drift pose
Drift budget: ≤ 10 mm over 10 minutes (SW-08), enforced by periodic LiDAR correction on top of continuous encoder+IMU odometry.
TF2 chain: map → odom → base_link → {lidar, imu, camera, standoff sensor}
Notes: Left column: go sensor by sensor, and for each one state both its contribution and its specific weakness — this shows the panel we understand failure modes, not just capabilities. Right side: this is the actual fusion architecture — encoder+IMU run continuously at high rate for the primary estimate, LiDAR corrects it periodically rather than being the primary source. Technical point: emphasize why LiDAR is a correction, not the primary source — flat walls give LiDAR few features to scan-match against, so leaning on it as the sole source would be fragile. Likely question: 'What happens to accuracy if LiDAR drops out entirely for the whole mission?' Strong answer: 'Encoder+IMU dead-reckoning continues, but after a configurable time/distance without correction the mission pauses and asks the operator to confirm before continuing, because drift risk to the ±20mm path-accuracy budget becomes unbounded.'

## Slide 8
HYBRID DESIGN
Autonomous AI Navigation
APR — Autonomous AI Navigation & Painting Control | Design Review
8
NOT this: Camera → Neural Network → Motors — unverifiable for a safety-critical wall-climbing robot.
CLASSICAL (deterministic)
Owns everything safety- and motion-critical
SLAM + Localization (EKF)
Costmaps (static + dynamic)
Coverage planning, path planning
Motion control
Safety state machine
AI / ML (perception only)
Advisory input to costmap — never wired to actuation
Obstacle/object classification
Environmental understanding
Optional predictive navigation (future)
Optional segment-order optimization (advisory)
Notes: Open with the red 'not this' box — naming the naive architecture explicitly and rejecting it up front pre-empts the most common reviewer assumption about 'AI navigation.' Then contrast the two columns: everything that touches safety or motion lives in the deterministic column; AI lives only in perception and feeds the costmap, same as any other obstacle input. Technical point: a wrong AI classification degrades gracefully — an unclassified object defaults to 'unknown, stop,' it doesn't degrade to an unsafe action. Likely question: 'Isn't that just calling it AI navigation for the pitch while it's really classical robotics?' Strong answer: 'Exactly — that's deliberate. AI does the one thing classical methods are weak at, open-set object classification, and nothing else. Overstating AI's role would be the presentation issue, not underusing it.'

## Slide 9
RUNTIME SAFETY
Obstacle Detection + Dynamic Replanning
APR — Autonomous AI Navigation & Painting Control | Design Review
9
Obstacle
detected
Spray
OFF
SAFE
STOP
Check safety
conditions
Replan
Resume when
safe
Known CAD obstacles
Excluded at planning time — never a runtime surprise
Unexpected obstacles
Costmap update, small local deviation, resumes automatically
Temporary obstacles
Immediate stop until cleared or operator confirms
Unsafe conditions
Escalates directly to Safety Supervisor, bypasses replanning
Notes: Top: this six-step flow is the exact sequence that fires the instant any obstacle is detected — walk it left to right, and land hard on the fact that spray cuts off before the stop even completes, not after. Bottom: four categories of obstacle, each handled differently — known CAD obstacles were already excluded when the coverage path was generated, so they're not even a runtime event. Technical point: the 'unsafe conditions' category (red) bypasses the normal replanning loop entirely and escalates straight to the Safety Supervisor state machine on slide 11. Likely question: 'How do you tell a temporary obstacle like a person apart from a permanent unexpected one like a pipe?' Strong answer: 'Classification confidence plus motion history from the perception node — and critically, low-confidence or person-class detections always default to the conservative full-stop path, never to 'replan and continue.''

## Slide 10
CLOSED-LOOP CONTROL
Standoff + Spray Control
APR — Autonomous AI Navigation & Painting Control | Design Review
10
STANDOFF CONTROL LOOP
Distance
sensor
Error =
target-actual
PI
controller
(20-50Hz)
Actuator
command
Target: 200–300 mm | Tolerance: ±20 mm
Standoff error is a direct gate on spray, not just a logged quality metric: too close → thick coat / runs; too far → thin coat / overspray.
SPRAY GATING LOGIC
✓ Valid trajectory
✓ Correct speed
✓ Correct standoff (≤20mm)
✓ Safe adhesion (vacuum nominal)
✓ Safety state = RUNNING
✓ No fault
ALL TRUE → SPRAY ON
ANY FALSE → SPRAY OFF
Notes: Left: standoff is a simple PI loop running at 20-50Hz — sufficient given the tolerance and slow approach speeds, no need for MPC on the first prototype. Right: this is a hard AND-gate, all six conditions must be true simultaneously, and it re-evaluates continuously, not just once per pass. Technical point: spray flow is also velocity-compensated — modulated to actual measured speed, not commanded speed, so a stall never causes a thick spot. Likely question: 'Why PI and not something more advanced like MPC?' Strong answer: 'The ±20mm tolerance at low approach speed doesn't justify MPC's complexity yet — if bench testing shows overshoot beyond tolerance, a feedforward term or full PID is the next step before MPC.'

## Slide 11
FAIL-SAFE DESIGN
Safety / Fail-Safe Architecture
APR — Autonomous AI Navigation & Painting Control | Design Review
11
INIT
SELF
CHECK
READY
RUNNING
FAULT
E-STOP
SAFE
SHUTDOWN
SAFETY OUTRANKS EVERYTHING
Higher priority than navigation, AI, motion, spraying
Can force FAULT / E-STOP from any state, any time
Only operator acknowledgment clears a FAULT — never automatic
E-stop target: hard-cut actuation within ≤ 0.5 s
8 MONITORED FAULT INPUTS
E-stop
Vacuum pressure
Tilt
Slip
Battery/power
Communication
Sensor health
Navigation health
Notes: Top: this is the full formal state machine — walk it once, left to right, note that FAULT and E-STOP can be entered from RUNNING at any time, not just sequentially. Left card: this is the single most important rule in the whole software design — read it near-verbatim, it's the answer to a huge fraction of reviewer safety questions. Right card: eight independently monitored inputs — mention that each one has a documented, specific response, not a generic 'stop everything' behavior. Technical point: the hardware E-stop line is intended to be independent of the software topic path where possible — flag this honestly as coordinated with, but not fully owned by, the software team. Likely question: 'Can AI ever clear a FAULT state automatically?' Strong answer: 'No — only explicit operator acknowledgment clears FAULT or EMERGENCY_STOP. That's a hard architectural rule, not a configurable option.'

## Slide 12
IMPLEMENTATION STACK
ROS 2 + Simulation Architecture
APR — Autonomous AI Navigation & Painting Control | Design Review
12
16 ROS 2 PACKAGES (apr_ws)
apr_description, apr_bringup
apr_hardware, apr_sensors (C++)
apr_localization, apr_mapping (C++)
apr_cad_processor, apr_mission_planner (Py)
apr_coverage_planner, apr_navigation
apr_obstacle_detection (Py, OpenCV/PyTorch)
apr_safety, apr_motion_controller (C++)
apr_spray_controller (C++)
apr_telemetry (Py) | apr_interfaces (IDL)
SIMULATION-FIRST WORKFLOW
Ubuntu 24.04
ROS 2 Jazzy
Gazebo Harmonic
APR URDF + virtual wall
SLAM → Nav2 → Coverage Planner
Autonomous simulated APR
Same nodes run against sim or real sensor data — only the driver layer (apr_hardware/apr_sensors) swaps.
Notes: Left: don't read every package name — point out the pattern instead: safety-critical packages (hardware, localization, safety, motion, spray) are C++; planning/CAD/telemetry are Python. Right: this is the exact simulation pipeline from base OS to an autonomous simulated rover — Gazebo Harmonic with a virtual vertical wall standing in for the real one. Technical point: land the callout text at the bottom hard — it's the reason simulation results are trustworthy: identical nodes, only the sensor/actuator boundary is re-pointed between sim and hardware. Likely question: 'How do you simulate vacuum adhesion in Gazebo?' Strong answer: 'Approximated with a high-friction or fixed joint standing in for the adhesion physics — we're explicit that this is a scoped simplification, not a first-principles vacuum model; adhesion-loss dynamics get validated on real hardware.'

## Slide 13
EXECUTION PLAN
Development Roadmap
APR — Autonomous AI Navigation & Painting Control | Design Review
13
Phase
0-3
Environment, ROS2 basics, sim robot, sensors
Phase
4-6
SLAM, EKF, Nav2, vertical-wall simulation
Phase
7-9
CAD processor, mission + coverage planner
Phase
10-12
Obstacle detection, standoff/spray, safety supervisor
Phase
13-14
Hardware-in-the-loop, controlled real-wall testing
Every phase has a written objective, task list, required software, test procedure, completion criteria, common mistakes, and an explicit “do NOT attempt yet” boundary — full detail in the written report, Part 16.
Notes: Present this as five stage-gates, not fifteen isolated tasks — group them the way the boxes are grouped: foundation, localization/nav, planning, execution control, hardware validation. Technical point: every single phase (all 15, detailed in the report) has an explicit 'do NOT attempt yet' list — this is intentional, to stop the team from building APR-specific logic on an unverified ROS2 base. Likely question: 'What's the biggest schedule risk in this roadmap?' Strong answer: 'Phase 12, the safety supervisor — it requires all 8 fault scenarios to be bench-tested before hardware-in-the-loop, and fault injection testing tends to surface edge cases late; we've budgeted it as its own phase rather than folding it into Phase 13 for exactly that reason.'

## Slide 14
VALIDATION
Testing and Validation
APR — Autonomous AI Navigation & Painting Control | Design Review
14
Unit
Module
Simulation
Integration
HIL
Low-wall
Small
area
Full
mission
Path accuracy
±20 mm / 1 m
Standoff
200-300 mm, ±20 mm
Coverage
≥90%, ≥10 m²/hr
Slip
≤10 mm / 10 min
Runtime
≥30 min continuous
Power
≤700 W peak
Safety (E-stop)
≤0.5 s
Overspray
≤10%
Notes: Top: this is the full test progression, seven stages from a single unit test up to a complete supervised mission — no stage is skipped, each gates the next. Bottom: eight KPIs, each with a hard numeric target — walk two or three you expect to be challenged on (path accuracy, E-stop, coverage) rather than reading all eight verbatim. Technical point: every KPI here is measured from a logged, timestamped ROS 2 topic via rosbag2 — never from operator estimation, which makes results reproducible and auditable. Likely question: 'What's your test procedure for the 0.5-second E-stop target specifically?' Strong answer: 'A timed hardware test — trigger E-stop, log the timestamp of the trigger and the timestamp of the last actuator command, and confirm the delta is under 0.5s across repeated trials, not just once.'

## Slide 15
FINAL INTEGRATED APR SOFTWARE SYSTEM
CAD
Wall Map
Mission +
Coverage Plan
Localized
Navigation
Standoff +
Spray
Obstacle Handling
(classical + AI)
Safety Supervisor
(highest priority)
Telemetry /
Dashboard
Auditable
KPI Log
WHAT THIS DESIGN GUARANTEES
AI never issues a motor, spray, or vacuum command directly
Every numeric target traces to WBS 1.1 / 1.2 and is independently testable
Safety Supervisor can halt any module from any state, at any time
Identical ROS 2 nodes run in simulation and on hardware — no logic rewritten
Thank you — questions welcome
Notes: This closing slide is the whole pipeline compressed to eight boxes — use it to remind the panel of the full end-to-end flow in under thirty seconds before opening for questions. Spend the remaining time on the four guarantee bullets — these are the four claims most likely to be re-tested by follow-up questions, so make sure each one was already demonstrated earlier in the deck, not asserted for the first time here. Technical point: this slide intentionally doesn't introduce anything new — a design review closing slide should summarize, not add scope. Likely question: 'If you had to cut one thing from this design to hit the timeline, what would it be first?' Strong answer: 'Predictive AI navigation and segment-order optimization — both are explicitly marked optional/advisory in this design, so they're the first things to defer without touching the safety-critical core.'